Lecture I-V summary

Knudsen number: K_n = "Mean free path " / " smallest length scale "

Shallow water equations: Assumption H << L and homogeneous (ρ=const.)
1. Use scaling to obtain hydrostatic equilibrium and incompressibility
2. Obtain ∇_H p = ρg∇_H η
3. Use continuity and BC to obtain {Dh} over {Dt} +h∇_H·u=0
Two layer model: Assumption same as before, note ∇_H p_0 = 0 .
1. Write NS equations with new continuity.
2. First layer same as before
3. The second layer uses continuous pressure. p_2 (z)=p_0 +ρ_1 g(η0-η1)+ρ_2 g(η_1-z)
4. Obtain reduced gravity g´=g {ρ_2 - ρ_1 } over {ρ_1}
Reduced gravity model: (aka 1.5) Assumption H2>>H1.
1. Notice that shallow part is much faster, u_2 ≈ 0
2. Obtain relation ∇_H η_0 ≈ -{g'}over{g}∇_H η_1
3. Set h_1 = η_0 - η_1 which gives g´ and h_1 for upper layer
Potential vorticity: Material invariance, assume shallow. Use 𝜁 = left({∂v}over{∂x} - {∂u}over{∂y}right) .
Note: All functions of Q are material invariants.

Linear wave solution: Assume SWE, f=f_0 and u=εu´, v=εv´, η=H+ε η’.
1. Neglect all ε² terms.
2. Apply Fouriers ansatz
3. Solve for ω(f,k,l)
4. Two solutions:
  1. ω=0 → Geostrophic
  2. ω≠0 → Pointcarté waves
5. Use c = sqrt{gH} and Rossby number of deformation L_D = c over {f_0} = sqrt{gH} over f_0 .
  1. If SW: ω>>f_0 → ω²=c²(k²+l²)
  2. if LW: ω≈f_0 “Internal oscillations"
Geostrophic adjustment: Assume linearized waves
1. Use equations to derive expression for 𝜁 (Q)
2. Begin by doing {∂(eq1)} over {∂x} + {∂(eq2)} over {∂y} = -g∇H²η
  1. Insert 𝜁 when possible
  2. Use continuity as {∂²η} over {∂t²} =-H {∂η} over {∂t} left [{∂u} over {∂x} +{∂v} over {∂x} right]
3. Split solution into homogeneous and particular as η = η_w (t) + η_p
4. Use the starting scenario to determine Q , use relation from before.
5. Use particular solution to derive η_p and determine geostrophic wind.